## Slide 1: Network Enabled Weapons – Complexities and Considerations
Justin Smith
3 - 5 September 2024 | Portsmouth University, UK
© 2024 ATEQ Consulting Ltd

## Slide 2: Disclaimer(s)!
The thoughts in this presentation are entirely “personal”:
  Not endorsed by any government entity
  Nor is this the ‘position’ of any of our International customers
  Intended to stimulate thoughts and possibly (hopefully!) debate

## Slide 3: NEW – The Standards
MIL-STD-6016F Change 1 – August 2017
ATDLP-5.16(B)(1) – October 2018
  Primary areas
    Section 5 –
      Part 2 – J11.0 / J11.1 / J11.2 Message Descriptions
      Part 4 Transmit & Part 5 Receive Tables – J11.0 / J11.1 / J11.2
    Appendix A – Imp Reqs (C2 & NonC2)
    Appendix X – NEW Transactions
Notes: Other areas – NEW PPLI, Mission Assignments, Engagement Status/BDA Reporting, etc

## Slide 4: NEW – What Is It ?
NOT JUST LAUNCH & CONTROL !!!
Other Controller
Back-Up Controller
3rd Party Information Providers

## Slide 5: Participants – Network Enabled Weapon
Network Enabled Weapon
Precision Guided Missile with the ability to communicate with other network participants
In accordance with the protocols defined in Appendix X of the Standard, Transmit and Receive Tables, etc

## Slide 6: Participants – Network Enabled Weapon
Network Enabled Weapon
Notes: MBDA – SPEAR - NETWORK ENABLED - PRECISION SURFACE ATTACK
Navair – Raytheons JSOW C1 - air-to-ground NEW capable of attacking stationary land & moving maritime targets.
Kongsberg - JSM – Joint Strike Missile
There are a variety of terminal variants (e.g. DLS TACNET, Harris BATS-E) and integration approaches (terminal or SDR)

## Slide 7: Participants – Control
Network Enabled Weapon
Current Controller
New Controller
The current controller is a network participant, designated prior to launch and not necessarily the launch platform. It has control authority to issue directives to the assigned weapon including retargeting the weapon to a new target, providing target updates & aborting the weapon.
Current controller responsibilities may be handed off to a different network participant – a New Controller.
The current controller can also assign the weapon various third parties, authorized to communicate with the weapon

## Slide 8: Participants – Third Party Source
Fully Authorized
Alternate Controller
IFTU 3PS
Ping Only IFTU 3PS
Network Enabled Weapon
An Alternate Controller is a 3PS with whom the weapon is authorized to communicate.
- Fully Authorized IFTU 3PS
- Ping Only IFTU 3PS
An IFTU 3PS is a 3PS who has been delegated target update authority. This IFTU 3PS has no other control authority.
The standards have growth potential to support future 3PS types. Not yet defined ?

## Slide 9: NEW – Imp Reqs

## Slide 10
Platform | Function
Alternate Controller
Ping Only 3PS
Fully Authorized IFTU 3PS
Missile Directives/Queries (J11.1)
Current Controller
WIFT QUERY DIRECTIVE
RETARGET DIRECTIVE
MISSION SUPPLEMENT DIRECTIVE
LOITER DIRECTIVE (Pre-Planned, Fixed, Immediate)
RESUME DIRECTIVE
ABORT DIRECTIVE (Pre-Planned, Fixed, Immediate)
EXCLUSION ZONE ABORT OVERRIDE DIRECTIVE
EMCON CHANGE DIRECTIVE
HANDOFF CONTROL CHANGE ORDER
THIRD PARTY COMMUNICATION CHANGE DIRECTIVE
HANDOFF - CHECK-IN RESPONSE
IN-FLIGHT TARGET UPDATE DIRECTIVE
IN-FLIGHT TARGET UPDATE DIRECTIVE SUPPLEMENT
HANDOFF - CHECK-IN RESPONSE
PING QUERY
IN-FLIGHT TARGET UPDATE DIRECTIVE
IN-FLIGHT TARGET UPDATE DIRECTIVE SUPPLEMENT
PING QUERY
HANDOFF - CHECK-IN RESPONSE
New Controller
Mandated
Mandated
Mandated
Mandated

## Slide 11
Function | Platform
Alternate Controller
Ping Only 3PS
Fully Authorized IFTU 3PS
Missile Responses (J11.0)
Current Controller
RETARGET DIRECTIVE RESPONSE
MISSION SUPPLEMENT DIRECTIVE RESPONSE
HANDOFF CONTROL CHANGE ORDER RESPONSE
3PS COMMUNICATION CHANGE DIRECTIVE RESPONSE
IN-FLIGHT TARGET UPDATE DIRECTIVE RESPONSE
LOITER DIRECTIVE RESPONSE
RESUME DIRECTIVE RESPONSE
ABORT DIRECTIVE RESPONSE
EZAO DIRECTIVE RESPONSE
EMCON CHANGE DIRECTIVE RESPONSE
HANDOFF - CHECK-IN
HANDOFF – CHECK-IN
PING QUERY RESPONSE
IN-FLIGHT TARGET UPDATE DIRECTIVE RESPONSE
PING QUERY RESPONSE
HANDOFF - CHECK-IN
New Controller
Optional
Optional
Optional
Optional
Optional
Optional
Optional
Optional

## Slide 12
Function | Platform
Alternate Controller
Ping Only 3PS
Fully Authorized IFTU 3PS
Missile Reports (J11.0)
Current Controller
BOMB HIT INDICATION (BHI) REPORT
BASIC WEAPON IN FLIGHT TRACK (WIFT) REPORT
WIFT SUPPLEMENT REPORT
SELF ABORT REPORT
CONTACT REPORT
New Controller
BOMB HIT INDICATION (BHI) REPORT
BASIC WEAPON IN FLIGHT TRACK (WIFT) REPORT
WIFT SUPPLEMENT REPORT
SELF ABORT REPORT
CONTACT REPORT
Optional
Optional
Optional
Optional
Optional
Optional
Optional
Optional

## Slide 13
Function | Platform
Function | Platform
Alternate Controller
IFTU 3PS
Weapon Coordination (J11.2)
CONTROL REQUEST FROM CURRENT CONTROLLER
CONTROL REQUEST TO CURRENT CONTROLLER
ACCEPT RESPONE
REJECT RESPONSE
HANDOFF FAILURE
New Controller
Current Controller
IFTU 3PS REQUEST FROM CURRENT CONTROLLER
IFTU 3PS REQUEST TO CURRENT CONTROLLER
ACCEPT RESPONE
REJECT RESPONSE
CEASE IFTU 3PS REQUEST FROM CURRENT CONTROLLER
Optional
Mandated
Mandated
Notes: Control
– All optional for Tx except Accept/Reject which are Tx if any of the other message are received.
- All optional for Rx except Accept/Reject which are Rx if any of the other message are transmitted
IFTU
- All optional for Tx
- IFTU 3PS request from current controller and Cease IFTU, only mandated MUs for reception.

## Slide 14: NEW – Messages in Context
J11.1
J11.1
J11.2
J11.2
J11.2
J11.1
J11.1
J11.1
J11.0
J11.0
J11.0
J11.2

## Slide 15: NEW – Imp Reqs

## Slide 16: Information Exchange Requirements

## Slide 17: NEW – Perfect Implementation

## Slide 18: NEW – Imp Reqs

## Slide 19: NEW – Actual Weapon Implementation

## Slide 20: NEW – Weapon Implementation

## Slide 21: NEW – Weapon Implementation

## Slide 22: NEW – Imp Reqs

## Slide 23: NEW – New Control

## Slide 24: NEW – SoS Caps & Lims

## Slide 25: NEW – SoS Caps & Lims

## Slide 26: Conclusions
Helping the User Navigate Network Enabled Weapons
  Agree which Systems are in scope
  Determine Requirements across the entire System of Systems
  Understand Mandated vs Optional Options within the Imp Reqs
  Ask suppliers for detailed Specification/Implementation Data
  Understand System Caps & Lims

## Slide 28: Credits
  ATDLP-5.16 Edition C Version 1 - March 2021
  https://www.mbda-systems.com/product/spear/
  https://www.rtx.com/raytheon/what-we-do/sea/joint-standoff-weapon
  https://www.kongsberg.com/kda/what-we-do/defence-and-security/missile-systems/joint-strike-missile-jsm/